## Cruise Checks – every 10 to 15 minutes SADIE
- Suction – green range
- Ammeter – green range, charge light off
- Direction Indicator – check aligned with compass
- Icing – carb. Heat on for 10-15 seconds
- Engine – oil temperature & pressure in the green range
- Fuel – pressure & contents, safe range, shut-off ON
- Mixture – fully rich or leaned for the cruise
- Ignition – check Both

## Stalling & Low Flying HASELL(L)
- Height – recover by 2500, in LFZ below 500’ AGL
- Airframe – check flaps set as required, undercarriage
- Security – no loose objects, hatches & harnesses secure
- Engine – check FMI
- Location – not above populated areas
- Lookout – for other aircraft, radio call if required
- Lights – for LFZ Nav & landing lights ON

# Stalling – between stalls HELL
- Height – recover by 2500, in LFZ below 500’ AGL
- Engine – check FMI
- Location – not above populated areas
- Lookout – for other aircraft, radio call if required