## Immediate Actions
- Convert excess speed to height
- Fuel pump ON
- Carb heat ON
- Squawk 7700 (simulate)
- Set glide attitude TRIM for 75 knots

## Plan Approach
- Estimate wind direction
- Select field – 7S 2W E
- size, shape, surface, slope, sun, surrounds, stock
- wind, wires
- elevation – make estimate
- 1/3rd point touchdown
- Estimate 1000’ area
- Estimate 1500’ area (top of downwind leg)
- Estimate elevation and note altimeter “dial” readings
Fly The Pattern : head for 1500’ area, do not lose sight of field

## Trouble Checks FMII
- Fuel : pump ON, shutoff ON, pressure, contents
- Mixture : fully rich
- Ignition : BOTH, try each mag, attempt restart
- Instruments : check T’s & P’s normal

Check/Warm Engine – throttle to 2000 RPM then back to idle

Fly The Pattern – check altitude: approaching 1500’ or 1000’ area

## Radio Call
- Mayday Mayday Mayday (simulate)
- xyz traffic / all stations
- callsign
- location, altitude
- description of problem
- intentions
- POB

Fly The Pattern – check altitude: downwind area

## Passenger Brief
- Describe the problem
- Describe your intentions
- Security brief : recall preflight brief
- Harness secure, remove sharp objects & glasses
- Brace for landing when ordered
- Designated meeting point eg. Nearest house

Check/Warm Engine – throttle to 2000 RPM then back to idle

Fly The Pattern – check altitude: prepare for finals

## Pre-landing Checks BUMFHW
- Brakes – check pressure, un-parked
- Undercarriage – Fixed
- Mixture – full rich, carb heat cold
- Fuel – pump on, check pressure, contents sufficient
- Hatches and harnesses all secure, secure loose objects
- Windsock – favoured runway

## Final Checks – Simulation
- Carb heat cold
- Mixture fully rich
- Go around : at or before 500’ AGL
- full power, carb heat cold, flaps 10˚
- nose to horizon, positive rate of climb @70knots
- 200’ AGL & clear of obstacles : flaps up, fuel pump off, climb attitude 75 knots

## Final Checks – Real
- Fuel OFF
- Mixture IDLE CUTOFF
- Ignition OFF
- Set flaps as & when required
- MASTER OFF